## Slide 1: Fulcher-α Spectra and Laser Photo-Detachment Measurements, and Models at SNU H- Source
10th International symposium on Negative Ions, Beams and Sources - NIBS'26
Jeong-Jeung Dang1, Jaeyoung Choi2, Kihyun Lee3, June Young Kim4, Kyoung-Jae Chung5, and Yong-Seok Hwang5
1 Department of Energy Engineering, Korea Institute of Energy Technology (KENTECH)
2 Display Research Center, Samsung Display,
3 Korea Atomic Energy Research Institute (KAERI),
4 Department of Semiconductor Engineering, Myongji University,
5 Department of Energy Systems Engineering, Seoul National University

## Slide 2: Outline
Introduction to the SNU H- Source
Optical and Laser Diagnostics for the SNU H- Source
Self-Consistent 1-D Modeling & Analysis
Recent Work on Novel H- Source Concepts
Summary

## Slide 3: Development Experience of SNU RF-TCP H⁻ Source
Introduction to the SNU H- Source
[1] Y. S. Hwang and G. H. Lee, RSI 71 (2000), 943-945.
[2] I. S. Hong, et al., AIP Conf. Proc. 639 (2003), 61-66.
[3] H. S. Jeong, et al., RSI 77 (2006), 03A536.
Stage 1: Establishing R&D Foundation (2000–2006)
  Concept and Set-up of Cs-Free Volume-Production H⁻ Source
  Introduced RF-TCP antenna outside dielectric window to prevent erosion & contamination [1]
  Extracted H⁻ beam for tandem accelerator injector [2]
  Controlled Te near extraction hole via dipole magnets in extractor: reduced e/H⁻ ratio to 8 [3]
Stage 2: Performance Enhancement via Hardware Modifications (2006–2014)
  Modifications of Potential Structures, Surface Materials, and Chamber Geometry
  Controlled local potential structure to be favorable for H⁻ extraction and introduced tantalum secondary electrode to boost surface production [4]
  Modified length and shape of source chamber to elevate driver Te and power density for increased H2(υ*) precursor generation [5, 6]
Stage 3: Diagnostic Systems & Physical Modeling (2015–Present)
  Strengthening Physical Analysis via H ⁻ Source Diagnostic & Coupled Modeling
  Established comprehensive diagnostic systems: OES (VDF measurement), laser photo-detachment (H⁻ density), and Langmuir probes (plasma parameters) [7, 8]
  Developed numerical models to figure out physical relationships between measured parameters and source performance [7]
[4] Y. An, B. Jung, Y. Hwang, RSI 81 (2010), 02A702.
[5] K. J. Chung, et al., RSI 85 (2014), 02B112.
[6] B. K. Jung, et al., RSI 85 (2014), 02B114.
[7] K. J. Chung, et al., New J. Phys. 18 (2016), 105006
[8] J. J. Dang, et al., RSI 87 (2016), 053503 (2016)

## Slide 4: Negative Ion Source (NIS) in SNU
Introduction to the SNU H- Source
Bias electrode
Plasma electrode
Extraction electrode
Acceleration electrode
13.56 MHz RF Power
Cusp
magnet
Virtual filter
magnet
Dipole filter magnet
Quartz window
3½ turns planar antenna
Operation Conditions
  Pressure : 0.4 - 4 Pa (H2)
  RF power : 0.5 - 1 kW
  Te : 5 - 10 eV (driver) 1 - 3 eV (extr.)
  ne : ~ 1018 m-3 (driver) ~ 1017 m-3 (extr.)
  n- : 1015 - 1016 m-3

## Slide 5: Configuration of Volume-Production NIS
Simultaneous Requirement of High and Low Te Regions
Introduction to the SNU H- Source
Part | Driver region | Extraction region
Role | Populating vibrationally excited hydrogen molecules | Producing H- ions & Preventing destruction

## Slide 6: Diagnostics for NIS in SNU
Optical and Laser Diagnostics for the SNU H- Source
Diagnostics
  Plasma parameters : Langmuir probe, Optical Emission Spectroscopy (OES)
  Vibrational states H2(υ*) : OES (Fulcher-α)
  Negative ion density (n-) : Laser photo-detachment

## Slide 7: Diagnostics for Vibrational State Distribution
Optical and Laser Diagnostics for the SNU H- Source
Method | Principle & Setup | Measurable States | Pros | Cons
CARS [1] | Two-color laser matching H2 vibrational resonance |  | Excellent spatial resolution | obscured by non-resonant background
VUV LIF [2] | Tunable VUV laser excitation and subsequent fluorescence detection |  | Absolute density, comprehensive coverage of all vibrational levels | Complex tunable VUV source, overlaps with plasma radiation
REMPI [3] | Multiphoton resonant excitation and photoionization |  | Excellent state selectivity | Cross-section uncertainty and laser saturation
OES + CR Model [4] | Fulcher-alpha band emission, CR model |  | Simple setup, in situ and real-time monitoring | quenched by predissociation
Method | Principle & Setup | Measurable States | Pros | Cons
CARS [1] | Two-color laser matching H2 vibrational resonance |  | Excellent spatial resolution | 
VUV LIF [2] | Tunable VUV laser excitation and subsequent fluorescence detection |  | Absolute density, comprehensive coverage of all vibrational levels | Complex tunable VUV source, overlaps with plasma radiation
REMPI [3] | Multiphoton resonant excitation and photoionization |  | Excellent state selectivity | Cross-section uncertainty and laser saturation
OES + CR Model [4] | Fulcher-alpha band emission, CR model |  | Simple setup, in situ and real-time monitoring | 
[1] M. Péalat, et al., J. Chem. Phys. 82 (1985), 4943-4953 [2] T. Mosbach, et al., PRL 85 (2000), 3420-3423 [3] P. J. Eenshuistra, et al., EPL 8 (1989), 423-427 [4] U. Fantz and B. Heger, PPCF 40 (1998) 2023-2032

## Slide 8: Vibrational States Diagnostics
Fulcher-α Band Spectrum
  Representative molecular band spectrum (approx. 590~650 nm) emitted via radiative transition of H2 from upper to lower Fulcher state.
    Q-branch spectrum (no change in rotational quantum number, 𝐽) utilized for diagnostics.
    P- and R-branches excluded from analysis due to transition probability uncertainties affected by other electronic states.
Optical and Laser Diagnostics for the SNU H- Source
Q1
Q2
Q3

## Slide 9: Vibrational States Diagnostics
Fulcher-α Spectroscopy
  Intensity Ratio and Vibrational Temperature,
    Density of state
    Intensity of respective spectra
    If vibrational state distribution of state is in Boltzmann distribution
Optical and Laser Diagnostics for the SNU H- Source
Q1
Q2
Q3

## Slide 10: Vibrational States Diagnostics
Fulcher-α Spectroscopy
  Required Fundamental Data to Determine Vibrational Temperature
    Vibrationally-resolved excitation cross sections and radiative transition probabilities
  Spectroscopic Limit: Restricted to v ≤ 3 due to predissociation (v' ≥ 4)
  Modeling Limit: Boltzmann assumption cannot capture non-Boltzmann distribution such as the suprathermal plateau.
  A need to develop a model covering non-Boltzmann vibrational distribution function (VDF)
Optical and Laser Diagnostics for the SNU H- Source
T. Mosbach, et al., PRL 85 (2000), 3420-3423
2006
1998
U. Fantz and B. Heger, PPCF 40 (1998) 2023-2032.
U. Fantz and D. Wünderlich, At. Data Nucl. Data Tables 92 (2006), 853-973.

## Slide 11: Other Parameters from Fulcher-α
Rotational Temperature and Gas Temperature
  The rotational temperature of d-state can be derived from the slope of the Boltzmann linear plot using measured spectra.
  Approximation to the rotational temperature of the ground state utilizing the physical relationship between energy states.
  Gas temperature estimation by assuming thermal equilibrium between rotational and translational modes due to rapid energy relaxation.
Optical and Laser Diagnostics for the SNU H- Source

## Slide 12: Other Parameters from Fulcher-α
Degree of Dissociation (DoD)
  Simultaneous measurement of atomic (H-γ) and molecular (Fulcher-α) emission intensities.
  Atom/molecule density ratio deduced from intensity ratio corrected by effective emission rates.
Optical and Laser Diagnostics for the SNU H- Source
U. Fantz et al., Nucl. Fusion 46 (2006), S297

## Slide 13: Negative Ion Density Measurement
Laser Photo-Detachment
  Measurement of negative ion density by collecting electrons detached from H- via Nd:YAG laser irradiation and detecting the induced current change
    Requirement to verify laser energy in the saturation regime to guarantee complete photo-detachment of all negative ions within the beam path.
    Determination of negative ion fraction from the ratio of the photo-detached current increment to the electron saturation current of the probe.
Optical and Laser Diagnostics for the SNU H- Source

## Slide 14: Motivation for Simulation Study
Contradiction of Diagnostic Results and Limitation of 0-D Model for VDF
  Contradictions in Fulcher-α diagnostics assuming a Boltzmann distribution (e.g., higher vibrational temperature in the low-Te extraction region), requiring a non-Boltzmann VDF treatment.
  Inability of the zero-dimensional (0-D) model to accurately reproduce the exact negative ion density peak at specific pressures, resulting in overestimation at high pressure regimes.
  Requirement for an integrated 1-D transport model coupling the generation of vibrationally excited molecules in the driver region with their collisional relaxation during transport to accurately evaluate the local VDF and negative ion density.
Recent Work on Novel H- Source Concepts
Tvib

## Slide 15: Self-Consistent 1-D Model for NIS

## Slide 16: List of Processes in Model
Recent Work on Novel H- Source Concepts

## Slide 17: Key Results of Simulation
Key Results of Simulation for Volume-Production NIS
  VDF Relaxation during Transport: Decay of highly vibrationally-excited molecules to lower states during transport from the driver to the extraction region.
  Dominant Collisional Quenching: Intensified VDF relaxation at high-pressure regimes driven by frequent vibrational-translational (V-T) energy transfer collisions with neutral particles.
  Correction of Overestimation: Successful correction of the negative ion density overestimation observed in 0-D model at high pressures.
Recent Work on Novel H- Source Concepts

## Slide 18: Summary of Volume-Production NIS Study
Mechanism of Optimum Pressure for H- Production
  Low-Pressure Limitations: High electron temperature is favorable for generating vibrationally excited molecules in the driver region. However, the absolute H- yield in the extraction region is restricted by lower plasma density and degraded dissociative attachment (DA) due to relatively high Te at extraction region.
  High-Pressure Limitations: Higher operating pressure increases plasma density and lowers Te, theoretically favoring the DA process. However, excessive pressure severely depletes the critical highly-excited precursor states during transport due to frequent V-T collisional quenching.
  Conclusion (Optimum Condition): The existence of an optimal pressure maximizing the absolute H- density is determined by a physical trade-off balancing the availability of H2 precursors and the mitigation of collisional VDF quenching, comprehensively validated by both experimental measurements and self-consistent 1-D modeling.
Recent Work on Novel H- Source Concepts

## Slide 19: Confinement-Driven H- Enhancement via Anode Spot
Recent Work on Novel H- Source Concepts
High Density H- Generation Mechanism
  Anode spot plasma: Generation of localized high ne and Te region via a positively biased electrode at low power.
  Volume-Production: Accelerated H2(𝜐*) generation via elevated Te , boosting internal H- yield.
  Potential-Driven Inflow: A steep potential structure actively pulls in and traps surrounding H- ions, dramatically boosting local density.
  Future Work: Optimization of operating conditions (e.g., pressure) and extraction geometries to harness as a practical ion source.
Jaeyoung Choi, et al., Plasma Sources Sci. Technol. 34 (2025) 025013

## Slide 20: Two-Region Arc Plasma (TRAP) Ion Source
Recent Work on Novel H- Source Concepts
Filter-Free Two-Region Separation
  TRAP Ion Source: DC arc-driven H-source developed by KAERI for NBI systems.
  Primary Electron Confinement: Shapes the magnetic field and adjusts movable filaments to strictly confine high-energy primary electrons within the upper chamber.
  Filter-Free Spatial Division: Achieves a hot driver and cold extraction region without a conventional transverse filter field, as only collisionally-cooled slow electrons flow downward.
  Future Work: Reinforcing negative ion diagnostics and developing comprehensive numerical models to understand primary electron behavior and the H- production mechanisms.
Kihyun Lee, et al., Nucl. Eng. Technol. 56 (2024) 3961–3968

## Slide 21: Summary
Summary of SNU H- Source Research & Recent Novel Concepts
  RF-TCP SNU H- Source: External antenna setup for contamination-free, long-lifetime CW operation based on a volume-production design.
  Diagnostics System: Langmuir Probe, Fulcher-α OES (VDF, Tgas, DoD), and Laser Photo-Detachment (H- density)
  1-D VDF Transport Model
    Developed to overcome the 0-D model's overestimation of H- density at high pressures.
    Incorporates the collisional relaxation of VDF during transport from the driver to the extraction region, showing high agreement with H- density measurements.
  Recent Novel Concepts
    Anode Spot (SNU): Utilizes local double-layer potential to induce inflow and maximize H- density.
    TRAP Ion Source (KAERI): A novel arc ion source that physically separates regions using optimized magnetic field structures and movable filament placement.
Summary

## Slide 22
10th International symposium on Negative Ions, Beams and Sources - NIBS'26
Thank You for Your Attention
Jeong-Jeung Dang
Department of Energy Engineering, KENTECH
Fusion pLASma Heating lab. (FLASH)
jjdang@kentech.ac.kr