## Slide 1: Design choices, implementation and status of the PIP-II Warm Front End
Lionel Prost
PIP-II Warm Front End L3 Manager
September Day, 2026

## Slide 2: Agenda
Fermilab Accelerator Complex & Proton Improvement Plan-II (PIP-II)
PIP-II Warm Front End (WFE)
  Guiding principle & design choices
  Validation at the PIP-II Injector Test (PIP2IT)
Installation status & Outlook

## Slide 3: Some Acronyms
AD: Accelerator Directorate
PIP-II: Proton Improvement Plan-II
PIP2IT: PIP-II Injector Test
CAM: Control Account Manager
LEBT: Low Energy Beam Transport
MEBT: Medium Energy Beam Transport
HEBT: High Energy Beam Transport
HBB: PIP-II’s High Bay Building
WFE: Warm Front End
LBNF: Long Baseline Neutrino Facility
DUNE: Deep Underground Neutrino Experiment
DOE: US Department of Energy
FNAL: Fermi National Accelerator Laboratory (a.k.a. Fermilab)
SRF: Superconducting RF
RF: Radio Frequency
RFQ Radio Frequency Quadrupole

## Slide 4: Fermilab Accelerator Complex

## Slide 5: Fermilab Accelerator Complex
National User Facility
Fermilab’s Accelerator Complex is one of 28 DOE Office of Science National User Facilities
Developed over 58 years, the Accelerator Complex comprises 5 particle accelerators and storage rings, 2 high-power target stations, several experimental areas and miles (kilometers) of beamlines

## Slide 6: PIP-II Mission
PIP-II is an essential upgrade to Fermilab accelerator complex to enable the world’s most intense beam of neutrinos to LBNF/DUNE, and a broad physics research program for decades to come
The PIP-II scope enables the accelerator complex to reach 1.2 MW proton beam on LBNF target
H- ion source
800MeV SRF Linac
Dump
25 kW Dump
Tevatron Tunnel
Beam Transfer Line
Booster
Cryo plant
PIP-II Scope
800 MeV H− SRF linac, to replace the 50+ year-old warm linac CW RF Operations
Linac-to-Booster transfer line
Accelerator Complex Upgrades:
Booster
Recycler
Main Injector
Conventional Facilities
PIP-II Capabilities
Beam Power
1.2 MW proton beam
Upgradeable to multi-MW
Flexibility, multi-user capability
CW-compatible
Customized beams
Multi-user delivery
Reliability
Modernizes Fermilab accel complex

## Slide 7: PIP-II Accelerator Overview
Defining parameters

## Slide 8: Boundary conditions
Acceleration in SRF cavities start at low energy (2.1 MeV vs. > ~100 MeV in most other superconducting pulsed linacs)
  Transition from ‘warm’ (i.e. normally conducting) technology and ‘cold’ (i.e. superconducting) technology is mostly dictated by RF power operational costs
  To first order, the higher the duty factor, the lower the transition (but there is no universal criterion)
CW operations economics
CW machines
Plot adapted from CERN Accelerator School 2013 (M. Vretenar)
SRF technology would not have been chosen if beam for LBNF/DUNE was the only goal

## Slide 9: Boundary conditions
Chart: Beam duty factor, %
| 1.25
J-PARC linac | 4e-06
LANSCE | 1.2255e-06
KOMAC | 6.25e-06
ESS | 2e-07
SNS (3 MW upgrade) | 3.3333e-07
PIP-II | 5.6818e-05 | 6.25e-07
Generally accepted loss requirements for “hands-on” maintenance: 1 W/m
  Exponential dependence as a function of energy
  ⇨ Fractional loss at 800 MeV (CW): ~10-6 m-1
CW operation implies stringent loss requirements (absolute)
“warm”
“cold”
1 W/m assumed or quoted
LBNF/DUNE operation
Ultimate goal
Chart: Energy (MeV)
| 3.1190217161667366 | 3.548487822674991 | 4.0370882198114098 | 4.5929652598480422 | 5.2253824364423869 | 5.9448787574726705 | 6.7634443738651058 | 7.6947203912051956 | 8.7542261939226993 | 9.959618070327183 | 11.330983448388571 | 12.891175645597615 | 14.666194711393977 | 16.685620708765782 | 18.983106655504876 | 21.596939339808891 | 24.570677356023094 | 27.953876993161384 | 31.802918072881116 | 36.181943499208451 | 41.163928177277292 | 46.831895114233262 | 53.280298968192668 | 60.616600101609421 | 68.963055370090288 | 78.458755489519177 | 89.261942933490701 | 101.55264898799096 | 115.53569390890689 | 131.44410017892437 | 149.54297574453014 | 170.1339319458842 | 193.56010976279848 | 220.21189813742487 | 250.53343966747306 | 285.03003208502912 | 324.27654886398989 | 368.92701928255053 | 419.72552758908978
J-PARC — 1 W/m | 0.00046635 | 0.00040991 | 0.0003603 | 0.00031669 | 0.00027836 | 0.00024467 | 0.00021506 | 0.00018903 | 0.00016615 | 0.00014604 | 0.00012837 | 0.00011283 | 9.9177e-05 | 8.7174e-05 | 7.6623e-05 | 6.735e-05 | 5.9198e-05 | 5.2034e-05 | 4.5736e-05 | 4.0201e-05 | 3.5335e-05 | 3.1059e-05 | 2.73e-05 | 2.3996e-05 | 2.1092e-05 | 1.8539e-05 | 1.6295e-05 | 1.4323e-05 | 1.259e-05 | 1.1066e-05 | 9.7266e-06 | 8.5494e-06 | 7.5147e-06 | 6.6052e-06 | 5.8058e-06 | 5.1031e-06 | 4.4855e-06 | 3.9426e-06 | 3.4655e-06
LANSCE — 1 W/m | 0.00024179 | 0.00021253 | 0.0001868 | 0.0001642 | 0.00014432 | 0.00012686 | 0.0001115 | 9.8008e-05 | 8.6147e-05 | 7.5721e-05 | 6.6556e-05 | 5.8501e-05 | 5.1421e-05 | 4.5197e-05 | 3.9727e-05 | 3.4919e-05 | 3.0693e-05 | 2.6978e-05 | 2.3713e-05 | 2.0843e-05 | 1.8321e-05 | 1.6103e-05 | 1.4154e-05 | 1.2441e-05 | 1.0936e-05 | 9.612e-06 | 8.4487e-06 | 7.4262e-06 | 6.5274e-06 | 5.7374e-06 | 5.043e-06 | 4.4327e-06 | 3.8962e-06 | 3.4246e-06 | 3.0102e-06 | 2.6459e-06 | 2.3256e-06 | 2.0442e-06 | 1.7968e-06 | 1.5793e-06 | 1.3882e-06 | 1.2202e-06 | 1.0725e-06 | 9.4268e-07
KOMAC — 1 W/m | 6.6794e-05 | 5.871e-05 | 5.1605e-05 | 4.5359e-05 | 3.9869e-05 | 3.5044e-05 | 3.0803e-05 | 2.7075e-05 | 2.3798e-05 | 2.0918e-05 | 1.8386e-05 | 1.6161e-05 | 1.4205e-05 | 1.2486e-05 | 1.0975e-05 | 9.6464e-06 | 8.4789e-06 | 7.4528e-06 | 6.5508e-06 | 5.7579e-06 | 5.0611e-06 | 4.4485e-06 | 3.9101e-06 | 3.4369e-06 | 3.0209e-06 | 2.6553e-06 | 2.334e-06 | 2.0515e-06
ESS — 1 W/m | 0.00012812 | 0.00011261 | 9.8982e-05 | 8.7003e-05 | 7.6473e-05 | 6.7218e-05 | 5.9082e-05 | 5.1932e-05 | 4.5647e-05 | 4.0122e-05 | 3.5266e-05 | 3.0998e-05 | 2.7246e-05 | 2.3949e-05 | 2.105e-05 | 1.8503e-05 | 1.6263e-05 | 1.4295e-05 | 1.2565e-05 | 1.1044e-05 | 9.7075e-06 | 8.5327e-06 | 7.5e-06 | 6.5923e-06 | 5.7944e-06 | 5.0931e-06 | 4.4767e-06 | 3.9349e-06 | 3.4587e-06 | 3.0401e-06 | 2.6721e-06 | 2.3487e-06 | 2.0645e-06 | 1.8146e-06 | 1.595e-06 | 1.402e-06 | 1.2323e-06 | 1.0831e-06 | 9.5205e-07 | 8.3683e-07 | 7.3555e-07 | 6.4653e-07 | 5.6828e-07 | 4.995e-07
SNS — 1 W/m | 0.00014062 | 0.0001236 | 0.00010864 | 9.5493e-05 | 8.3936e-05 | 7.3777e-05 | 6.4848e-05 | 5.7e-05 | 5.0101e-05 | 4.4037e-05 | 3.8708e-05 | 3.4023e-05 | 2.9905e-05 | 2.6286e-05 | 2.3105e-05 | 2.0308e-05 | 1.785e-05 | 1.569e-05 | 1.3791e-05 | 1.2122e-05 | 1.0655e-05 | 9.3653e-06 | 8.2319e-06 | 7.2356e-06 | 6.3599e-06 | 5.5902e-06 | 4.9136e-06 | 4.3189e-06 | 3.7962e-06 | 3.3368e-06 | 2.9329e-06 | 2.5779e-06 | 2.2659e-06 | 1.9917e-06 | 1.7507e-06 | 1.5388e-06 | 1.3525e-06 | 1.1888e-06 | 1.045e-06 | 9.1849e-07 | 8.0733e-07 | 7.0962e-07 | 6.2373e-07 | 5.4825e-07
PIP-II (CW) — 1 W/m | 0.00016031 | 0.00014091 | 0.00012385 | 0.00010886 | 9.5687e-05 | 8.4106e-05 | 7.3927e-05 | 6.498e-05 | 5.7115e-05 | 5.0203e-05 | 4.4127e-05 | 3.8786e-05 | 3.4092e-05 | 2.9966e-05 | 2.6339e-05 | 2.3151e-05 | 2.0349e-05 | 1.7887e-05 | 1.5722e-05 | 1.3819e-05 | 1.2147e-05 | 1.0676e-05 | 9.3843e-06 | 8.2486e-06 | 7.2503e-06 | 6.3728e-06 | 5.6015e-06 | 4.9236e-06 | 4.3277e-06 | 3.8039e-06 | 3.3435e-06 | 2.9389e-06 | 2.5832e-06 | 2.2705e-06 | 1.9957e-06 | 1.7542e-06 | 1.5419e-06 | 1.3553e-06 | 1.1913e-06 | 1.0471e-06 | 9.2035e-07 | 8.0897e-07 | 7.1106e-07 | 6.25e-07
PIP-II (LBNF) — 1 W/m | 0.014573 | 0.01281 | 0.011259 | 0.0098966 | 0.0086988 | 0.007646 | 0.0067206 | 0.0059072 | 0.0051923 | 0.0045639 | 0.0040115 | 0.003526 | 0.0030993 | 0.0027242 | 0.0023945 | 0.0021047 | 0.00185 | 0.0016261 | 0.0014293 | 0.0012563 | 0.0011042 | 0.00097059 | 0.00085312 | 0.00074987 | 0.00065911 | 0.00057934 | 0.00050923 | 0.0004476 | 0.00039342 | 0.00034581 | 0.00030396 | 0.00026717 | 0.00023483 | 0.00020641 | 0.00018143 | 0.00015947 | 0.00014017 | 0.00012321 | 0.0001083 | 9.5189e-05 | 8.3669e-05 | 7.3542e-05 | 6.4642e-05 | 5.6818e-05
For LBFN/DUNE (1.1% duty factor) → ~10-4 m-1 at 800 MeV

## Slide 10: PIP-II Warm Front End (WFE)

## Slide 11: Warm Front End scope
It is composed of:
  Two Ion Sources (IS) and a Low Energy Beam Transport (LEBT)
    DC/long pulse operation
  RFQ (162.5 MHz)
    CW operation (RF)
    30 keV ⇒ 2.1 MeV
  Medium Energy Beam Transport (MEBT)
    Nominal output current: 2 mA averaged over ~ms (from ms to CW operation)
    Bunch-by-bunch chopping capability
WFE prepares a H- beam optimized for injection into the Booster and provides capabilities for future CW operation
IS & LEBT
RFQ
MEBT
Tunnel

## Slide 12: Ion Source
Baseline requirements
  DC, H-, 10 mA at 30 keV ⇨ D-Pace’s TRIUMF Type 15 mA H- Volume-Cusp
Filament driven (~300 hours filament lifetime) ⇨ frequent changeout needed
Robust and proven commercial solution
Y-configuration
Significant electron current is ‘dumped’ onto extraction electrode assembly (and surrounding ‘baffles’) ⇨ may affect long term operation reliability and equipment longevity
DC operation is not necessary for LBNF/DUNE
Developed pulsing of the ion source itself

## Slide 13: Low Energy Beam Transport (LEBT)
Design determining factors
  Optical matching (a, b) at RFQ entrance
  Capability of tuning the beam line with short pulses representative of long pulse operation (i.e. constant beam parameters throughout the pulse) ⇨ Transport scheme with un-neutralized region (next slide)
A long LEBT for tuning flexibility, vacuum management and operational robustness
2 solenoids
3 solenoids
High vacuum pressure
  Gas load from ion source
Neutralizing particles confined by potential barrier
Potential barrier
Low vacuum pressure
  Vacuum pumping station
  Limits rate of production of neutralizing particles
Clearing electric field
  Sweeps neutralizing particles out of the beam
Scheme of LEBT with un-neutralized section requires transition from (nearly) fully neutralized to (nearly) fully un-neutralized to take place where the beam current density is uniform
PIC-like simulations through one solenoid
  Initial distribution has a uniform current density distribution but Gaussian in the velocity space

## Slide 14: Transport scheme validation at PIP2IT
RFQ
Beam profile and emittance measurements in LEBT
PIP2IT was a nearly full replica of the PIP-II front-end (WFE + first 2 cryomodules) with all envisioned features
Beam parameters (current, normalized emittance, a, b) measured downstream of the RFQ over a 500 ms pulse
Potential barrier
1D beam profiles at the scrapers. Dashed curves are fits, assuming a uniform (green) or a Gaussian (red) distribution, normalized to give the same integral
Phase space distributions for 2 different focusing solutions but same ion source tune
Small beam parameter variations measured in MEBT
Emittance scanner

## Slide 15: Low Energy Beam Transport (LEBT)
Design determining factors
  Avoid/minimize bombardment of RFQ vanes
    ⇨ No direct line of sight from the source
    ⇨ Addition of multiple aperture restrictions (Electrically Isolated Diaphragms a.k.a. EID)
    ⇨ Robust chopper, which includes a dedicated absorber
A long LEBT for tuning flexibility, vacuum management and operational robustness
Bending dipole magnet
Space/length
Central component of Machine Protection System (MPS) for inhibiting beam
2.1 m

## Slide 16: Neutrals and protons
Single stripping → Fast neutrals (~10% of H- beam current near ion source)
  Ballistic flight
Double stripping → Protons (~0.5% of H- beam current near ion source)
  Same envelope as H-
Electron stripping in H- collisions with gas immediately downstream of ion source extraction region
Proton area
Neutrals area
Noise area
1/12/16 data
x, mm
x’, mrad
Estimated with Allison scanner
H-
H0
H+
Bending magnet naturally ‘filters’ them out

## Slide 17: Medium Energy Beam Transport (MEBT)
Design determining factors
  Bunch-by-bunch chopping system
A long MEBT for bunch-by-bunch chopping and SRF protection
2 kickers
Large & complicated absorber capable of sustaining 21 kW of beam power continuously
Long (~50 cm) restricting apertures
Additional protection (entrance & exit) needed from transverse tails and/or erratic beam
Lattice needs to accommodate two (2) optics solutions/trajectories (passing and ‘to be removed’ bunches)
Kickers
Absorber assembly

## Slide 18: Bunch-by-bunch chopping at PIP2IT
Any bunch from initially CW sequence can be either removed or passed (6.15 ns bunch spacing ⇨ maximum switching frequency = 81.25 MHz)
Driver electronics maximum average switching frequency is 500 kHz
Example of an arbitrary pattern
Measured extinction between bunches <510-4 limited by instrumentation resolution/noise

## Slide 19: Medium Energy Beam Transport (MEBT)
Design determining factors
  Protect SRF from beam far tails and erratic beam loss
  Protect SRF from high vacuum section (absorber in particular) and vacuum incident
A long MEBT for bunch-by-bunch chopping and SRF protection
Extensive collimation system
Four (4) sets of transverse movable scrapers arranged in pairs separated by ~p/2 phase advance
Differential Pumping Insert (DPI) + beamline ‘buffer’ + Fact Acting Valve (FAV)
Another long aperture restriction (20 cm x ⏀1cm vs. ⏀3cm ) which complicates transport optics
MEBT scraper assembly
  Scraper is made out of TZM (Molybdenum alloy) Radiation cooled, electrically isolated
DPI
FAV

## Slide 20: Validation and Demonstration at PIP2IT
Differential Pumping Insert (DPI)
  Provides 2-4 decades of isolation
  In conjunction with Fast Acting Valve (FAV) → <10-6 torr liter of gas passes through FAV independently of leak size (up to atmosphere) upstream of DPI
DPI
FAV
Warm valve to HWR
2.1 m
0.9 m
Insignificant in terms of monolayer coverage on the cavity surfaces
Particle free practices during assembly
PIP2IT setup

## Slide 21: Medium Energy Beam Transport (MEBT)
Design determining factors
  Ion Source/LEBT access while running (→ IS maintenance) and WFE beamline visible by the public (→ administrative choice)
  Extensive suite of diagnostics
    Emittance scanner
    Ring Pick Ups (RPU)
    ACCTs, DCCT
    Beam Position Monitors
    Resistive Wall Current Monitor
    Wire-scanners
    Laser wire
    Fast Faraday Cup (FFC)
  All other features already mentioned
A long MEBT for bunch-by-bunch chopping and vacuum management
Radiation shielding wall separating warm section from SRF section
One more complication for the design of the optics although not an aperture restriction
Very long beamline (13 m)
Tunnel
RPU

## Slide 22: Particle free region at PIP2IT
DPI
FAV
Warm valve to HWR
2.1 m
0.9 m
PIP2IT setup

## Slide 23: Particle free region at PIP-II
Extended to accommodate radiation shield wall
  FAV to HWR distance maintained
  Moved scraper assembly upstream of DPI → Only moving devices are the vacuum valves
Moved components and extended w.r.t. PIP2IT
DPI
FAV
Warm valve to HWR
3.2m
0.9m
Empty section for radiation shield wall

## Slide 24: Installation status & outlook

## Slide 25: From PIP2IT WFE to PIP-II WFE
New redesigned ion source power cabinets
New/updated diagnostics (ACCT, DCCT, RWCM, emittance scanner)
New water jacket downstream of MEBT absorber for better heat management of beam tube from secondaries bombardment
Upgraded actuator assemblies for MEBT scrapers
New bunching cavities (same design)
New production kicker drivers (small upgrade)
New MEBT girders/stands
Some shuffling of components (no change to the beamline optics)
Small but important differences from lessons learned

## Slide 26: Fabrication/installation status
RFQ was the first component moved from PIP2IT to the PIP-II HBB
  Sets the ‘origin’ of the beam line
Started to expand the beamline both upstream and downstream
Cables pulled in August/September → Final alignment of LEBT and most of MEBT girders
  Beamline configuration for WFE commissioning does not include “particle-free” region → Physical air gap + temporary Faraday Cup upstream of bunching cavity 3 to allow for continuation of cryomodules installation during early beam operation
High-Bay Building (HBB) ready for installation of first beamline components in June
Particle-free region

## Slide 27: Diaporama

## Slide 28: Diaporama

## Slide 29: Diaporama

## Slide 30: Diaporama

## Slide 31: Diaporama

## Slide 32: Outlook
Warm Front End beam commissioning starts in 1 year from now

## Slide 33: Acknowledgement
This manuscript has been authored by Fermi Forward Discovery Group, LLC under Contract No. 89243024CSC000002 with the U.S. Department of Energy, Office of Science, Office of High Energy Physics
Thank you

## Slide 36: Backup slides

## Slide 37: Fermilab Accelerator Complex
Arial overview